## Slide 1: Action Items
WRF/LES model coupling
Model-measurement comparison
Forward modeling activities: consistency among the models

## Slide 2: Greenhouse Gas Emissions from the Baltimore-Washington Area: Initial Results from the WINTER 2015 flights
FLAGG-MD Meeting
Xinrong Ren
April 27, 2015

## Slide 3: Outline
Winter flight overview
A typical flight on 2/20/2015 (RF5)
CO2 and CH4 flux estimation
Preliminary Intercomparison with Purdue’s Duchess
Summary

## Slide 4
UMD Cessna 402B Research Aircraft
GPS Position (Lat, Long, Altitude)
Met (T, RH, P, wind speed/direction)
Trace gases:
O3: UV Absorption
SO2: Pulsed Fluorescence
CH4/CO2/CO/H2O: Cavity Ringdown, Picarro
NO2: Cavity Ring Down, Los Gatos
NO: Chemiluminescence
Aerosol Optical Properties:
Scattering: bscat (@450, 550, 700 nm), Nephelometer
Absorption: bap (565 nm), PSAP
Black Carbon: Aethalometer
Data Acquisition: 1 Hz
Aerosol Inlet
Gas Inlet
Met Sensors
New Picarro CO2/CH4/CO/H2O analyzer

## Slide 5
Flight Tracks, all flights

## Slide 6
Flihgt # | Date | Takeoff (UTC) | Landing (UTC) | Met Conditions
RF1 | 02/06/15 | 19:15:40 | 22:17:37 | WSW winds, PBL H=2000 ft
RF2 | 02/13/15 | 19:09:08 | 22:37:39 | WNW winds, PBL H=5000 ft
RF3a | 02/16/15 | 16:11:50 | 19:34:28 | WNW winds, PBL H~6000 ft, with Duchess
RF3b | 02/16/15 | 20:28:38 | 20:47:54 | 
RF4a | 02/19/15 | 16:49:04 | 18:55:38 | WNW winds, PBL H=4000 ft, with Duchess
RF4b | 02/19/15 | 19:55:51 | 22:26:16 | 
RF5a | 02/20/15 | 16:25:32 | 18:39:35 | WNW winds, PBL H=4000 ft
RF5b | 02/20/15 | 20:01:24 | 22:39:16 | 
RF6a | 02/23/15 | 18:08:11 | 20:14:17 | NNW winds, PBL H=4500 ft
RF6b | 02/23/15 | 21:08:59 | 23:33:04 | 
RF7 | 02/24/15 | 16:58:13 | 19:10:42 | S winds, PBL H=3000
RF8a | 02/25/15 | 16:10:49 | 18:25:48 | W winds, PBL H=5500 ft
RF8b | 02/25/15 | 19:22:30 | 21:41:20 | 
RF9 | 02/26/15 | 18:58:18 | 21:07:05 | NNW winds, PBL H=4000 ft
Flight Met Conditions

## Slide 7
VP
Missed approach
wind
Missed approach
VP
VP
VP
A typical mass balance experiment flight on 2/20/15

## Slide 8: A typical mass balance experiment flight on 2/20/15
VP
Missed approach
VP
VP

## Slide 9: 3 Downwind Vertical Profiles
Mixing layer depth ~3500 - 4000 ft

## Slide 10: CO2 Map
Dickerson
Brandon Shores
Easton
wind
Morgantown
Chalk Point
Power plant plumes clearly observed on the downwind transects.
TAPPA
ODESA

## Slide 11: CH4 Map
wind
Brown
Station
Landfill
High CH4 levels aloft at SW of the upwind leg: CH4 emissions from fracking?
TAPPA
ODESA
Easton

## Slide 12: CH4 vs. CO2 colored with SO2
Free troposphere
Power plants
Landfill
Urban
[SO2], ppbv

## Slide 13: CO2 on 2 downwind transects along the latitude
DC
plume
Baltimore
plume
Morgantown
Chalk Point
Brandon Shores

## Slide 14: CH4 on 2 downwind transects along the latitude
DC
plume
Baltimore
plume
Much larger CH4 enhancement in the DC plume than in the Baltimore plume.

## Slide 15: Estimation of CO2 and CH4 Fluxes
[C] : concentrations (downwind)
[C]b : concentration in background
U⊥ : perpendicular wind speed
Mass Balance Experiment (MBE) approach:
Flux
Baseline

## Slide 16: Estimation of CO2 and CH4 Fluxes
Flight # (Date) | Flux(CH4) (mol s-1) (M tons yr-1) | Flux(CO2) (tons s-1) (M tons yr-1)
RF2 (2/13/2014) | 512 0.26 | 6.9 217
RF4 (2/19/2014) | 1356 0.68 | 4.8 152
RF5 (2/20/2014) | 914 0.46 | 6.0 190
RF6 (2/23/2014) | 1550 0.78 | 9.4 295
RF7 (2/24/2014) | 1100 0.56 | 9.5 300
RF8 (2/25/2014) | 1304 0.66 | 8.6 272
Mean | 1100±370 0.57±0.18 | 7.5±1.9 238±60
Note: (1) Errors in the last row are the standard deviations of fluxes.
(2) Mean concentrations at the edges of downwind transects (outside
of the urban plumes) are used as the background concentrations.
(3) Transect averaged perpendicular wind speeds are used.
(4) The population in the Balt–DC area is close to 10 million.

## Slide 17: Uncertainty Associated with the MBE Approach
Mass Balance Experiment (MBE) approach:
Mixing layer height (zi): ~10%
Plume width (x): ~5%
∆[C] = [C] – [C]b: ~20%
Perpendicular wind speed (U⊥): ~20%
Combined uncertainty in flux estimation: ~30%
Flux

## Slide 18: Cessna-Duchess Intercomparison Flight 2/16/2015

## Slide 19: CO2 and CH4 time series 2/16/2015
side-by-side flying

## Slide 20: WS and WD time series 2/16/2015
side-by-side flying

## Slide 21: WS Comparison 2/16/2015

## Slide 22
Successfully conducted MBE flights in the Balt-DC area in winter 2015
Preliminary estimation of GHG fluxes:
F(CH4): 1100±370 mole s-1 (or 0.57±0.18 million tons CH4/yr)
F(CO2): 7.5±1.9 tons s-1 (or 238±60 million tons CO2/yr)
Preliminary Cessna-Duchess intercomparison results: encouraging but need to look into reasons behind the discrepancies.
Future work will involve:
  Evaluating assumed boundary conditions.
  Using the kriging interpolation to build a concentration wall to improve flux estimation;
  Comparison with Ensemble Kalman Filter Assimilation modeling with high resolution WRF modeling.
Summary

## Slide 24: Extra Slides

## Slide 25
CO2 on flight track

## Slide 26
CH4 on flight track

## Slide 27
CO on flight track

## Slide 28: CO2/SO2 Peaks Observed and Nearby Power Plants in Indy 2014

## Slide 29: Power Plant Emission Validation (Indy 2014): ΔSO2/ΔCO2: Observed vs. Reported
Flight | Plume Source (Power Plant) | Hour (LST) | ΔSO2/ΔCO2 (observed) (%) | ΔSO2/ΔCO2 (reported) (%) | WS (m/s) | Distance from power plant (miles)
RF3_Peak 1 | Eagle Valley station | 14 | 0.09 | 0.76 | 3.1 | 28.3
RF3_Peak 2 | Eagle Valley station | 15 | 0.08 | 0.76 | 1.5 | 27.8
RF3_Peak 3 | Eagle Valley station | 16 | 0.1 | 0.76 | 4.1 | 31.6
RF5 | Harding Street station | 14 | 0.07 | 0.25 | 12.8 | 21.3
RF6 | Eagle Valley station | 13 | 0.13 | 0.79 | 12.8 | 3.3

## Slide 30: Ozone and NO2 time series 2/16/2015
side-by-side flying