## Slide 1: AOSC 620 Tropospheric Ozone
History – meteorology vs. chem.
Theory – models
In Situ measurements
Remote sensing
Policy relevant science.
Ozone is a major pollutant. It does billions of dollars worth of damage to agricultural crops each year and is the principal culprit in photochemical smog. Ozone, however, exists throughout the troposphere and, as a major OH source and a greenhouse gas, plays a central role in many biogeochemical cycles. That photochemical processes produce and destroy stratospheric ozone have been recognized since the thirties, but the importance of photochemistry in tropospheric ozone went unrecognized until the seventies.

## Slide 2: From The Lancet Commission on pollution and health, 2018
Pollution is the largest environmental cause of disease and premature death in the world today. Diseases caused by pollution were responsible for an estimated 9 million premature deaths in 2015 —16% of all deaths worldwide — three times more deaths than from AIDS, tuberculosis, and malaria combined, and 15 times more than from all wars and other forms of violence.

## Slide 3
The classical view of tropospheric ozone was provided by Junge (Tellus, 1962) who looked at all the available ozone observations from a handful of stations scattered over the globe. Free tropospheric concentrations appeared to be fairly uniform, but boundary layer concentrations were reduced. He also noticed a repeating annual cycle with spring maxima and fall minima. Tropospheric ozone maxima lagged stratospheric maxima by about two months. From this he concluded that ozone is transported from the stratosphere into the troposphere where it is an essentially inert species, until it contacts the ground and is destroyed. The implied residence time varies from 0.6 to 6.0 months.
Source – Stratosphere
Sink – Surface deposition
Chemistry – Little or none
Lifetime 0.6 to 6.0 mo

## Slide 4
Levy (Planet. Space Sci., 1972) first suggested that radicals could influence the chemistry of the troposphere, and Crutzen (Pageoph, 1973), shortly followed by Chameides and Walker (J. Geophys. Res., 1973), pointed out that these radical reactions could form ozone in the nonurban troposphere. Chameides and Walker’s model predicted that the oxidation of methane (alone) in the presence of NOx would account for all the ozone in the troposphere and that ozone has a lifetime of about 1 day. Chatfield and Harrison (J. Geophys. Res., 1976) countered with data that show the diurnal variation of ozone in unpolluted sites is inconsistent with a purely photochemical production mechanism and showed that meteorological arguments could explain most of the observed ozone trends described by Chameides and Walker.
Radical View
Source – CH4 + NOx + hn
Sink – Surface and Rxn with HOx
Lifetime – 1 d
Image from Pasadena, CA 1973
(Finlayson-Pitts and Pitts, 1977).

## Slide 5
To summarize, chemists found a possible major anthropogenic perturbation of a vital natural process. In their zeal to explain this problem some of the chemists completely neglected the physics of the atmosphere. This irritated some meteorologists, who point out that one can equally well interpret the observations in a purely meteorological context. With the dust settled, we can see that the physics of the atmosphere controls the day-to-day variations and the general spatial structure, but chemistry can perturb the natural state and cause long term trends. This paradigm recurs.

## Slide 7
Monthly mean afternoon (1 to 4 PM) surface ozone concentrations calculated for July using Harvard GEOS-CHEM model.

## Slide 8: What was the ozone concentration in the pre-industrial atmosphere?
Volz and Kley Nature (1988)
  In the 19th century, Albert-Levy bubbled air through a solution of iodide and arsenite.
  2I- + O3 + AsO33- → O2 + AsO43- + I2
  To measure the amount of iodine produced by ozone they titrated with iodine solution and starch as an indicator.

## Slide 9
The absolute value is now much higher, even in rural areas near France; Arkona is an island in the Baltic.
The seasonal cycle has shifted toward summer.
Volz and Kley attributed this to increased NOx emissions.

## Slide 10
Schematic overview of O3 photochemistry in the stratosphere
and troposphere.
From the EPA Criteria Document for Ozone and Related Photochemical Oxidants, 2007.

## Slide 11
Total (trop + strat) Ozone

## Slide 12: Jet Streams on March 11, 1990 Hotter colors mean less column ozone.

## Slide 13: TROPOSPHERIC Ozone Photochemistry
13
CLEAN AIR
(1) O3 + h  O2 + O(1D)
(2) O(1D) + H2O  2OH
(3) OH + O3  HO2 + O2
(4) HO2 + O3  2O2 + OH
-----------------------------------------
(3+4) 2O3  3O2 NET

## Slide 14
14
DIRTY AIR
(3') OH + CO  H + CO2
(4') H + O2 + M  HO2 + M
(5') HO2 + NO  NO2 + OH
(6') NO2 + h  NO + O
(7') O + O2 + M  O3 + M
-------------------------------------------------
(3'-7') CO + 2 O2  CO2 + O3 NET

## Slide 15: SIMILAR REACTION SEQUENCE FOR METHANE
CH4 + OH® CH3 + H2O
CH3 + O2 + M® CH3O2 + M
CH3O2 + NO® NO2 + CH3O
CH3O + O2 ® H2CO + HO2
HO2 + NO® NO2 + OH
NO2 + hn ® NO + O
O + O2 + M® O3 + M
--------------------------------
CH4 + 4O2 + hn ® 2O3 + H2CO + H2O NET

## Slide 16
2H2CO + hn ® H2 + CO
® HCO + H
H + O2 + M® HO2 + M
HCO + O2 ® HO2 + CO
------------------------------
2H2CO + 2O2 ® 2CO + 2HO2 + H2
What is the fate of formaldehyde?
The grand total is 4 O3 per CH4 oxidized!

## Slide 17: What constitutes sufficient NO to make ozone photochemically? HO2 + O3  2O2 + OH (4) HO2 + NO → NO2 + OH (5) When R4 = R5 then k4[O3] = k5[NO] and production matches loss. This happens around [NO] = 10 ppt

## Slide 18: Chain terminating steps: NO2 + OH + M → HNO3 + M HO2 + HO2 → H2O2 + O2
These reactions remove radicals and stop the catalytic cycle of ozone production. Definitions: NOx = NO + NO2
NOy = NOx + HNO3, + HNO2 + HO2NO2 + PAN + N2O5 + RONO2 + NO3- + …
NOz ≡ NOy - NOx

## Slide 19
EKMA.
Empirical Kinetic Modeling Approach, or EKMA. See Finlayson & Pitts page 892.

## Slide 20: The lifetime of hydrocarbons decreases with chain length and with points of unsaturation.
CH3-C6H4-CH3
Methane CH4
Ethane CH3CH3
Propane CH3CH2CH3

## Slide 21: Isoprene (2methyl butadiene) The world’s strongest emissions.

## Slide 22: Isoprene (2 methyl butadiene) Oxidation
Methyl vinyl ketone

## Slide 23: Criteria Pollutant Ozone, O3
Secondary
Effects:
1. Respiration - premature aging of lungs (Bascom et al., 1996); mortality (e.g., Jerrett et al., 2009).
2. Phytotoxin, i.e. Vegetation damage (Heck et al., JAPCA., 1982;
Schmalwieser et al. 2003; MacKinzie and El-Ashry, 1988)
3. Materials damage - rubber
4. Greenhouse effect (9.6 m)
Limit: was120 ppb for 1 hr. (Ambient Air Quality Standard)
75 ppb for 8 hr as of 2010
70 ppb for 8 hr as of 2015.
Ozone is an EPA Criteria Pollutant, an indicator of smog.
Ozone regulates many other oxidants

## Slide 24: Destruction by Dry Deposition
O3
Height
Deposition Velocity – the apparent velocity (cm/s) at which an atmospheric species moves towards the surface of the earth and is destroyed or absorbed.
Vd = H/Ĉ dC/dt
Where H = mixing height (cm)
Ĉ = mean concentration (cm-3)
C = concentration (cm-3)

## Slide 25: Destruction by Dry Deposition
O3
Height
From the deposition velocity, Vd, and mixing height, H, we can calculate a first order rate constant k’.
k’ = Vd /H
For example if the deposition velocity is 0.5 cm/s and mixing height at noon is 1000 m the first order loss rate is lifetime is 0.5/105 s-1 = 5x10-6 s-1 and the lifetime is 2x105 s or 56 hr (~2.3 d). At night the mixed layer may be only 100 m deep and the lifetime becomes 5.6 hr.
Deposition velocities depend on the turbulence, as well as the chemical properties of the reactant and the surface; for example of plant stomata are open or closed. The maximum possible Vd for stable conditions and a level surface is ~2.0 cm/s.

## Slide 26: Tech Note
X
Height
For species emitted into the atmosphere, the gradient is reversed (black line) and the effective deposition velocity, Vd, is negative. From the height for an e-folding in concentration, we can calculate the eddy diffusion coefficient (units m2/s)
1/k’ = t = H/ Vd = H2/Kz

## Slide 27: Trop Ozone: take home messages thus far.
Deposition velocity: Vd = H/Ĉ dC/dt
Where H = mixing height (cm)
Ĉ = mean concentration (cm-3)
C = concentration (cm-3)
k’ = Vd /H = 1/t
Kz = Eddy Diffusion Coefficient (m2/s)
Characteristic diffusion time: t = H2/Kz
Global mean Kz ~ 10 m2s-1, so the average time to tropopause
~ (104m)2/10(m2s-1) = 107 s = 3 months
Compare this to updraft velocities in Cb.
In convectively active PBL Kz ~ 100 m2 s-1

## Slide 28: Photochemical smog: The story of a summer day
Minimum
Early AM
Maximum
Early Afternoon
Temperature
Altitude
Temperature
Altitude
 Noct. inv.
Regulatory Ozone Season: May 1 to Sept 30
Rural Ozone
28
Notes: Summertime Ozone goes through a cycle every day: driven by meteorology (lots of light = high temps) and low winds
Under high pressure: production-destruction => this cycle as observed….mimimum when loss has continued for many hours unbalanced by production (no sun), sunrises production resumes to the point where production = destruction, just after local solar maximum (noon)
High pressure means air is sinking, therefore no clouds…so lots of sunlight, light winds, and emissions are “capped”
At night the structure of the atmosphere evolves to favor long range transport on regional scales (100’s to 1000 of km)
Power plants emit directly into the residual layer (at least ones with tall stacks) and this gets tranpsorted long distances and makes more pollutants that get mixed down later…
So power plants are imporant, and they are very important on large scales as a result of this chemistry and meteorology.
28

## Slide 29: The diurnal evolution of the planetary boundary layer (PBL) while high pressure prevails over land. Three major layers exist (not including the surface layer): a turbulent mixed layer; a less turbulent residual layer which contains former mixed layer air; and a nocturnal, stable boundary layer that is characterized by periods of sporadic turbulence.

## Slide 30
Two Reservoir Model (Taubman et al., JAS, 2004)
Cumulus
Cumulus
SO2
H2SO4

## Slide 32: Ozone is a national problem
32
(85 ppb)
Areas of the continental U.S. that are not in attainment of the 2015 8-hour O3 standard of 70ppb.

## Slide 33
Standard: 8 hr average 75 ppb

## Slide 35
What is the major natural source of ozone to the troposphere? Tropopause folds also called stratospheric intrusions.

## Slide 36: Tropopause folds - a natural source of ozone. Surface weather chart showing sea level (MSL) pressure (kPa), and surface fronts.

## Slide 37: Vertical cross section along dashed line (a-a’) from northwest to the southeast (CYYC = Calgary, Alberta; LBF = North Platte, NB; LCH = Lake Charles, LA). The approximate location of the jet stream core is indicated by the hatched area. The position of the surface front is indicated by the cold-frontal symbols and the frontal inversion top by the dashed line. Note: This is 12 h later than the situations shown in previous figure

## Slide 38: Since WWII, natural sources and sinks are << anthropogenic.
How many molecules of ozone are formed before NOx is converted to a less reactive state?

## Slide 39: Slope = 4-7 ppb O3/ppb NOz Measured values of O3 and NOz (NOy – NOx) during the afternoon at rural sites in the eastern United States (grey circles) and in urban areas and urban plumes associated with Nashville, TN (gray dashes); Paris, France (black diamonds); and Los Angeles CA (Xs). Sources: Trainer et al. (1993), Sillman et al. (1997, 1998), Sillman and He

## Slide 40: Main components of a comprehensive atmospheric chemistry modeling system, such as CMAQ.

## Slide 41
41
Empirical Kinetic Modeling Approach, or EKMA. See Finlayson & Pitts page 892.
Where is western MD?

## Slide 42: Space-borne NO2 reveals urban NOx emissions
Herman et al., NCAR Air Quality Remote Sensing from Space, 2006
Tropospheric NO2 columns derived from SCIAMACHY measurements, 2004.
The NO2 hot-spots coincide with the locations of the labeled cities.

## Slide 43
• OMI nitrogen dioxide data indicate a 30-40% decrease in the pollutant’s levels from 2005 to 2011.
• NO2 levels have dropped through the implementation of emission control devices on coal-burning power plants and more fuel-efficient cars.
• NASA AQAST members are working with state air quality agencies to demonstrate the effectiveness of their efforts to improve air quality and to find novel uses of satellite data for air quality applications.
NASA Aura OMI Shows Air Quality is Improving
Notes: US NOx emissions have decreased by about 50% since 2000 through a combination of controls on power plants and automobiles. For instance, see http://earthobservatory.nasa.gov/IOTD/view.php?id=83923 for a description of the impact of emission control device on
The Ozone Monitoring Instrument (OMI) is on the Aura satellite (http://aura.gsfc.nasa.gov), which just celebrated 10 years since launch.
The OMI NO2 data shown in the images were produced by the NASA GSFC OMI Science Team (614). The retrieval algorithm was developed by Lok Lamsal (GSFC; 614) and the data processed by Yasuko Yoshida (GSFC; 614), both of whom were partially funded by the NASA Air Quality Applied Sciences Team (AQAST) via Bryan Duncan (AQAST member). The images were created by the NASA Goddard's Scientific Visualization Studio/T. Schindler.
OMI data also show that sulfur dioxide (SO2), a precursor to acid rain and sulfate aerosols, has decreased significantly in the US over the Aura record: http://earthobservatory.nasa.gov/IOTD/view.php?id=76571

## Slide 45
The Tropospheric Ozone Assessment Report:
A community-wide effort to quantify tropospheric ozone in a rapidly changing world
Owen Cooper
CIRES, U. of Colorado/NOAA Earth System Research Lab., Boulder
owen.r.cooper@noaa.gov
Updated September, 2017

## Slide 48
A vector indicates the linear trend at a station for the period 2000-2014.
Warm colors indicate increasing ozone while cool colors indicate decreasing ozone.
The legend shows the p-Values on the linear trends associated with each vector, as indicated by the shading.
Statistically significant trends at the 95% confidence interval are shown on top in dark red and dark blue.
Medium orange and blue provide an indication of a trend.
Light orange and blue provide a weak indication of change.
Green indicates weak or no change.

## Slide 52
Nighttime lights of the world in 1992
Global population (United Nations): 5.5 billion
DMSP-OLS nighttime lights (V4) detected by The Defense Meteorological Satellite Program: http://ngdc.noaa.gov/eog/dmsp/downloadV4composites.html
Data collected by US Air Force Weather Agency, processed by NOAA NGDC and plotted by Owen Cooper, CIRES, U. of Colorado/NOAA ESRL

## Slide 53
Nighttime lights of the world in 2013
Global population (United Nations): 7.2 billion (30% increase)
DMSP-OLS nighttime lights (V4) detected by The Defense Meteorological Satellite Program: http://ngdc.noaa.gov/eog/dmsp/downloadV4composites.html
Data collected by US Air Force Weather Agency, processed by NOAA NGDC and plotted by Owen Cooper, CIRES, U. of Colorado/NOAA ESRL

## Slide 54: Ozone much improved in Maryland.

## Slide 55: Response to VOC controls Essex, MD (Urban); box model calc’s from Roberts, Salawitch, Wolfe et al. Ozone production rates (gross) 10:00-14:00

## Slide 56: Modeled rate of production of ozone in the Balt/Wash area went up before it went down. When region-wide NOx controls worked. Roberts et al. in prep (2019).
Time
Response to VOC controls Essex, MD (Urban); box model calc’s from Roberts, Salawitch, Wolfe et al. Ozone production rates (gross) 10:00-14:00

## Slide 57
How has (will) pollution ozone respond to climate change?

## Slide 58
58
Response of ozone to Maximum temperature measured in Baltimore. 1994-2004
Notes: 58

## Slide 59: Looking deeper into the data: method
5%
25%
50%
75%
95%
3°C
Temperature Binning
Ozone rises as temperature increases
The slope is defined to be the
“climate penalty factor”
59
Notes: Or “taking apart the blob”
Conditional distributions constructed using 3C temperature bins.
Plotted at midpoint of each temperature bin.
Results are relatively Insensitive to bin size (less than 0.1 ppb/C difference)
Regress each percentile separately.
Average the slopes.
“Wouldn’t you know, ozone distriubutions behave like republicans and walk in lock step.”
59

## Slide 60
Notes: 60

## Slide 61
Notes: 61

## Slide 62
Notes: 62

## Slide 63
Notes: 63

## Slide 64
Notes: 64

## Slide 65
Notes: 65

## Slide 66
Notes: 66

## Slide 67
Notes: 67

## Slide 68: Can we observe the influence of warming on air quality?
68
95%
75%
5%
50%
25%
Climate Penalty Factors
Consistent
across the distribution
AND
across the power plant
dominated receptor regions

## Slide 69: Can we observe the influence of warming on air quality?
69
Bloomer et al., Science, 2008
In Review
Reducing NOx emissions
Lowered
Ozone over the entire distribution
And decreases
the Climate Penalty Factor
The change in the
climate penalty factor is
remarkably consistent across
receptors dominated by
power plant emissions. Ignoring
SW:
The average of
3.3 ppb/°C pre-2002
Drops to
2.2 ppb/°C after 2002
95%
75%
5%
50%
25%
Notes: 69

## Slide 70: Measurement Model Comparison: NO2

## Slide 71: Ratio CMAQ/OMI

## Slide 72
December 2013, the Supreme Court heard arguments on the Cross-State Air Pollution Rule, CSAPR.
DISCOVER-AQ data went into an Amicus Brief.
Notes: In August 2012, a federal appeals court in DC overturned the Cross-State Air Pollution Rule that laid out how much air pollution states would have to clean up to avoid incurring violations in downwind states. The EPA appealed and the US Supreme Court heard arguments in December 2013. DISCOVER-AQ data were used in an Amici Curiae brief submitted to the Supreme Court. Air entering the eastern seaboard is often already in violation of the NAAQS for O3 and contains enough NO2 to generate more O3.

## Slide 73
Life as a Downwind State

## Slide 74
UMD Cessna in RAMMPP during DISCOVER-AQ flew spirals over a larger area.
AM PM
FME
Southerly Transport
Westerly Transport
EZF
UMD Cessna
Notes: NEEDS FREDERICKSBERG
74

## Slide 75: Published results
1. Ozone is a regional problem and reservoir species extend the lifetime of NOx. NO2 is high enough to generate new ozone at ~3 ppb/hr at midday even upwind of Baltimore and Washington. Brent et al., Atmos. Chem., (2013).
West
East
West
East

## Slide 76: Key Concepts
Both meteorology and photochemistry play important roles in local and global ozone chemistry.
Transport from the stratosphere represents a natural source of ozone.
VOC’s plus NOx make a photochemical source.
HOx reactions and dry deposition are sinks.
The lifetime of a species in the mixed layer is the H/Vd.
Greenhouse gas – for spectroscopy lecture.

## Slide 77: Impact of model resolution.
Much of the transport of smog is in the LFT.
CMAQ with 12 km resolution cannot resolve the elevated O3 reservoir of ozone, but with 4 km it can. Important to NOAA/ARL AQ forecast.
He et al., Atmos. Environ., 2014
12 km CMAQ  4 km CMAQ 