## Slide 1: Methane Emissions from the Baltimore-Washington Area: Airborne Observations and Comparison with Inventories
Xinrong Ren, Jonathan Hansford, Doyeon Ahn, Ross Salawitch, and Russ Dickerson (UMD)
Olivia Salmon and Paul Shepson (Purdue Univ.)
Outline
Aircraft measurements and mass balance approach for CH4 emissions
Comparison with CH4 Emission inventories
CH4 emissions based on CO & CO2 inventories and observed CH4/CO & CH4/CO2 ratios

## Slide 2
UMD Cessna & Purdue Duchess Research Aircraft
GPS Position (Lat, Long, Altitude)
Met (T, RH, P, wind speed/direction)
Trace gases:
O3: UV Absorption, modified TECO
SO2: Pulsed Fluorescence, modified TECO
CH4/CO2/CO/H2O: Cavity Ringdown, Picarro
NO2: Cavity Ring Down, Los Gatos
NO: Chemiluminescence, modified TECO
VOCs: grab canisters/GC-FID
Aerosol Optical Properties:
Scattering: bscat (@450, 550, 700 nm), Nephelometer
Absorption: bap (565 nm), PSAP
Black Carbon: Aethalometer
Aerosol Inlet
Gas Inlet
Met Sensors
UMD Cessna
Purdue Duchess
GPS Position (Lat, Long, Altitude)
Met (T, RH, P, 3-D wind by BAT)
2
Trace gases:
O3: UV Absorption, 2B Technology
CH4/CO2: Cavity Ring Down, Picarro
NO2: Cavity Ring Down, Los Gatos

## Slide 3
FLAGG-MD Flights during Winter 2015 and 2016

## Slide 4
Different Flight Patterns in Winter 2015 and 2016
Flights on 2/19/2015
Cessna
Duchess
Flights on 2/19/2016
Cessna
Duchess
wind
wind
Duchess
Cessna
Cessna
Duchess
FLAGG-MD 2015:
Both aircraft did leveled transects
FLAGG-MD 2016:
The Cessna did continuous vertical profiles downwind.
The Duchess did upwind survey & leveled transects downwind.
Longitude (°)

## Slide 5: Mass Balance Approach to Estimate Emission Rates
E. R. : emission rate
[C] : concentrations (downwind)
[C]b : concentration in background
U⊥ : perpendicular wind speed
Mass Balance Experiment (MBE) approach:
Background
Background
CO2, CH4, CO
Urban
CO2, CH4, CO
∆x
∆z

## Slide 6: Estimated GHG Emissions from the Baltimore-Washington Ares
Date | Flux(CO2) (moles s-1) | Flux(CH4) (moles s-1) | Flux(CO) (moles s-1)
02/08/16 | 73,200 | 418 | 430
02/12/16 | 93,000 | 350 | 510
02/17/16 | 107,800 | 1,078 | 365
02/18/16 | 98,100 | 373 | 611
02/19/16 | 142,800 | 722 | 688
Mean±1σ | 103,000 ±25,600 | 588±312 | 521±131
Flight Date | Flux(CO2) (moles s-1) | Flux(CH4) (moles s-1) | Flux(CO) (moles s-1)
2/6/15 | 94,500 | 557 | 521
2/13/15 | 71,000 | 290 | 281
2/18/15 | 91,200 | 795 | --
2/19/15 | 156,800 | 932 | 567
2/20/15 | 118,100 | 518 | 753
2/23/15 | 107,900 | 641 | 417
2/24/15 | 110,300 | 476 | 640
2/25/15 | 108,500 | 602 | 571
2/27/15 | 78,800 | 540 | --
Mean±1σ | 104,000 ±25,000 | 595±184 | 536±152
FLAGG-MD winter 2015
FLAGG-MD winter 2016
Mean CH4 emission rate: 592 ± 248 moles s-1

## Slide 7: CH4 Emissions from the SW Marcellus
Flight Date | [CH4]upwind (ppbv) | [CH4]downwind (ppbv) | WS (m s-1) | WD (deg) | PBL Height (m AGL) | CH4 E.R. (moles s-1)
8/25/15 | 1,967±22 | 2,023±39 | 9.7±1.4 | 260±12 | 2,200 | 2,391
8/29/15 | 2,016±16 | 2,119±50 | 6.6±1.4 | 226±13 | 1,950 | 2,315
9/14/15 | 1,960±28 | 2,032±37 | 9.6±1.2 | 283±12 | 1,500 | 2,156
From Marcellus (55x77 km): 2,287 ± 120 moles CH4 s-1
From Balt-DC (75x95 km): 592 ± 248 moles CH4 s-1
Mass Balance Experiment (MBE) approach:
Prevailing
wind

## Slide 8: Point Source: CH4 Emissions from Brown Station Landfill
Flight # CH4 Emission Rate (moles s-1)
RF1 57.4
RF2 55.7
RF4 51.8
RF5 64.7
RF6 65.3
RF7 36.0
RF8 69.1
-----------------------------------
Mean 57.1 ± 11.1
wind
E. R. : emission rate
[C] : concentrations (plume peak)
[C]b : concentration in background
U⊥ : perpendicular wind speed
Brown Statin Landfill
A factor of 3.7 higher than the value in GHGRP
EPA GHGRP CH4 emission rate for this landfill: 15.5 moles s-1

## Slide 9: Mass Balance vs. Inventories
Landfill (# of transects/flights) | Mass Balance Flux Range** (moles CH4 /s) - Average of all transects | 2015 EPA (moles CH4/s) | 2014 MDE (moles CH4/s) | 2012 Maasakkers (moles CH4/s)
Brown Station (21/7) | 24.6 – 64.0 | 3.44 or 15.5* | 6.14 | 8.52
Eastern Sanitary (3/1) | 9.9 – 49.5 | 4.54 | 6.85 | 10.01
Quarantine Road (7/3) | 1.35 – 2.94 | 3.33 | 17.6 | 3.11
Harford Waste (2/2) | 2.22 – 8.50 | 5.42 | 3.52 | 5.52
Reichs Ford (3/2) | 12.8 – 26.2 | 5.88 | 1.83 | 4.96
Route 40 West (3/3) | 2.66 – 10.01 | 6.89 | 10.23 | 6.70
* EPA GHGRP requires landfills with a gas collection system (Brown Station has a gas collection system) to estimate their emissions in two ways. Typically, the higher of the two results is reported as the “official” value, but in Brown Station’s case, the lower number (3.44) was reported instead of the higher number (15.5).
**Flux range computed by varying horizontal transect width by 10% and PBL height by one-sigma.

## Slide 10: Gridded US CH4 NEI for 2012 (0.1° x 0.1°)
196 moles CH4/s
from Balt-DC

## Slide 11: CH4 Emissions from Sources in Balt-DC in CH4 NEI 2012
Landfills are a major CH4 source.
CH4 emissions from NG system may be under-estimated.
49%, 1.54 kg/s
12%, 0.39 kg/s
11%. 0.36 kg/s
10%, 0.30 kg/s
8%, 0.24 kg/s
8%, 0.24 kg/s
2%, 0.07 kg/s

## Slide 12: EDGAR4.2 Global 0.1° x 0.1° CH4 Emission Inventory 2010
Data source: http://edgar.jrc.ec.europa.eu/gallery.php?release=v42FT2010&substance=CH4&sector=TOTALS
The total CH4 emissions in the yellow rectangle (an approximately surveyed area) is 421 moles CH4 s-1.
Issues with EDGAR emissions: mainly allocated based on population instead of source locations.

## Slide 13: CH4 Emission Estimate using CH4/CO Ratio and CO Emissions
CH4:CO = 1.94
CH4:CO = 0.838
CH4:CO = 1.24
Total CO emissions from Balt-DC in EDGAR v4.3 2010: 0.459 MMtons/yr
The total CH4 emissions based on CH4 to CO ratio: 642 moles CH4 s-1 (436 – 1,003 moles CH4 s-1)
FLAGG-MD winter 2015

## Slide 14: CH4 Emission Estimate using CH4/CO2 Ratio and CO2 NEI 2014
CH4:CO2 = 1.60%
Total CO2 emissions from Balt-DC in NEI2014: 89.0 MMtons/yr
The total CH4 emissions based on CH4 to CO2 ratio: 583 moles CH4 s-1 (293 – 1,029 moles CH4 s-1)
CH4:CO2 = 0.909%
CH4:CO2 = 0.465%
FLAGG-MD winter 2016

## Slide 15: CO to CO2 ratio: Observed vs. EDGAR Emissions
Observed CO to CO2 molar ratio = 0.53% (black line)
CO to CO2 molar ratio in EDGAR 2010 emission inventory: 0.59% (red dashed line)
CO/CO2 ratio in EDGAR 2010
Obs. CO/CO2
in winter 2016

## Slide 16: CH4 Emissions from the Balt-DC Area: Top-down vs. Bottom-up
Top-down
Bottom-up
Top-down & Bottom-up
Maasakkers et al. [2016]
MD
DC
VA
in DC-Balt

## Slide 17
Successfully conducted mass balance flights for GHG in the Baltimore-Washington area in winter 2015 & 2016.
Estimated total emissions of CH4 from this area:
595±184 moles CH4 s-1 in winter 2015
588±312 moles CH4 s-1 in winter 2016
Major CH4 sources in the area: landfills and NG system.
Compared to CH4 emission inventories:
  Observed CH4 emissions are higher than the US NEI 2012 by a factor of 3
  higher than the state EI by a factor of ~2
  higher than the EDGAR 2010 by a factor of 1.4.
  Observed CH4 emissions is similar to CH4 emissions inferred from CO and CO2
  NEI with observed CH4/CO and CH4/CO2 ratios
Summary

## Slide 18
Date Assimulation Using HYSPLIT: Collaboration with NOAA/ARL
Tianfeng Chai and Ariel Stein (NOAA/ARL)
Method
A variational data assimilation method is used to find the sources with which HYSPLIT would reproduce concentrations that match best with the observations.
Assumptions
The two landfills causes for the measured excess CH4.
The CH4 emissions of the landfills vary each hour.
Two major limitations
There are other sources that contribute to the excess CH4.
Meteorological fields in the HYSPLIT dispersion model has uncertainties.
Ongoing work
To add more sources + constant emissions from landfills
To use ensemble runs to include uncertainties of meteorological fields

## Slide 19
Acknowledgements
NIST for funding
The flight crew at University Research Foundation
Winston Luke and Paul Kelley at NOAA/ARL
Jerry Rhoderick, Bob Miller, and Kimberly Schuldt at NIST
Acefaw Belay and David Krask at MDE
Students who were involved in the study
Notes: With that I would like to acknowledge the funding agencies for this projects as well as many people who helped including several students from UMD who helped to conduct flights.

## Slide 21
Extra Slides

## Slide 22: CH4 Emission Estimate using CH4/CO2 Ratio and CO2 NEI 2014
CH4:CO2 = 1.12%
Total CO2 emissions from Balt-DC in NEI2014: 89.0 MMtons/yr
The total CH4 emissions based on CH4 to CO2 ratio: 6.6 kg CH4 /s (3.5 – 11.6 kg CH4/s)
Cold winter in 2015
expected more CO2 emissions due to heating
A larger inferred CH4 emission rate
CH4:CO2 = 0.635%
CH4:CO2 = 0.336%
FLAGG-MD winter 2015

## Slide 23: CH4 Emission Estimate using CH4/CO2 Ratio and CO2 NEI 2014
CH4:CO2 = 1.12%
Total CO2 emissions from Balt-DC in NEI2014: 89.0 MMtons/yr
The total CH4 emissions based on CH4 to CO2 ratio: 6.6 kg CH4 /s (3.5 – 11.6 kg CH4/s)
Cold winter in 2015
expected more CO2 emissions due to heating
A larger inferred CH4 emission rate
CH4:CO2 = 0.635%
CH4:CO2 = 0.336%
FLAGG-MD winter 2015

## Slide 24: CH4 Emission Estimate using CH4/CO Ratio and CO Emissions
CH4:CO = 2.58
CH4:CO = 0.75
CH4:CO = 1.43
Total CO emissions from Balt-DC in EDGAR v4.3 2010: 0.459 MMtons/yr
The total CH4 emissions based on CH4 to CO ratio: 11.8 kg CH4 /s (6.2– 21.4 kg CH4/s)
FLAGG-MD winter 2016

## Slide 25: Observed C2H6-to-CH4 Ratio
Mean C2H6-to-CH4 ratio in natural gas of Baltimore Gas & Electric: 0.1045
Other major CH4 sources (landfills, enteric fermentation, waste water treatment) has little ethane emissions.
Emissions from the NG system account for 32% (2015) and 41% (2016) of total CH4 emissions.
FLAGG-MD winter 2015
FLAGG-MD winter 2016

## Slide 26: CH4 Emission Estimate from Unaccount-for NG
Total NG delivered to the Balt-DC area in February 2015: 54,495 million CF in Feb. 2015.
Lost & unaccounted-for (LAUF) NG : 3.34% of total NG delivered (PHMSA data)
Total lost & unaccounted for (LAUF) gas : 12.9 kg CH4/s
Not all LAUF gas is leaked into the atmosphere because besides leaks, unaccounted-for gas is also due to gas theft, accounting & meter errors, etc.
The worth of the LAUF gas = 54,495 x 106 CF x 3.34% x $0.012/CF
= $22 M in Feb. 2015

## Slide 27: Facility level CH4 Emissions in EPA’s GHGRP (excluding emissions from Petroleum & NG System )
Mostly landfills
The total CH4 emissions (other than the NG system) from the yellow rectangle is 1.21 kg/s
Based on the unaccounted-for natural gas and other CH4 sources in GHGRP, the total CH4 emission rate from the Balt-DC area:
12.86 + 1.21 = 14.07 kg/s
This may overestimate CH4 emissions since not all LAUF gas is emitted into the atmosphere.

## Slide 28: CH4 Emissions from the Balt-DC Area: Top-down vs. Bottom-up
Top-down
Bottom-up
Top-down & Bottom-up
Maybe upper limit

## Slide 29: Brown Station – Mass Balance Calculations
RF | Mass Balance Flux (moles / s) (Mean of flux calculated on each individual transect)
1 | 30.7
2 | 44.7
4 | 31.9
5 | 59.9
6 | 21.1
7 | 71.8
8 | 66.3
Mean ± St. Deviation | 46.6 ± 18.3

## Slide 30: Mass Balance – CH4 from DC/Baltimore
Flight Date | Emission Rate (moles CH4 s-1) | Emission Uncertainty Range – Horizontal Bounds* (moles CH4 s-1) | Flux Uncertainty Range – PBL Depth** (moles CH4 s-1) | Flux Uncertainty Range – Horizontal Bounds & PBL Depth Combined*** (moles CH4 s-1)
2/13/15 | 193 | 177 – 201 | 145 – 241 | 133 – 251
2/19/15 | 1260 | 1230 – 1270 | 853 – 1670 | 830 – 1680
2/20/15 | 509 | 452 – 509 | 351 – 667 | 311 – 667
2/23/15 | 157 | 141 – 169 | 110 – 204 | 99.0 – 219
2/24/15 | 951 | 857 – 1180 | 705 – 1200 | 633 – 1490
2/25/15 | 183 | 172 – 187 | 97.5 – 269 | 90.6 – 274
Mean | 542 | 505 – 586 (-6.8% / +8.1%) | 377 – 709 (-30.% / + 31%) | 349 – 764 (-36% / +41%)
*Flux range computed by varying horizontal transect width by 10%
**Flux range computed by varying PBL height by one-sigma
***Flux range computed by varying horizontal transect width by 10% and PBL height by one-sigma.

## Slide 31
CH4 emissions from King George Landfill
Brown Station
Quarrantine Rd
Eastern Sanitary
King George
[CH4] (ppbv)
11.5 km

## Slide 32
Estimate of CH4 Emissions from King George Landfill
[C] : concentrations (downwind)
[C]b : concentration in background
U⊥ : perpendicular wind speed
Mass Balance Experiment (MBE) approach:
CH4 emission rate from King George landfill based on a single downwind transect:
24.0 moles CH4 s-1 , or 12,100 tons CH4 yr-1
This is close to EPA’s GHGRP CH4 emission data for this landfill:
11,800 tons CH4 yr-1