## Slide 1
Model drivers Models Assimilation Observations
Carbon data assimilation strategy for urban GHG Monitoring
(Dickerson et al. 2014, proposal to NIST)

## Slide 2: Components of urban carbon modeling/DA system Modeling
WRF-Chem for atmospheric CO2 transport
  WRF: GFS global boundary forcing + other info by WRF pre-prosessor (WFS)
  WRF: Yonsei PBL scheme; Kain-Fritsch cumulus scheme (issue with mass flux? Sha Feng PSU), non 1km domain
  Use ensemble for transport uncertainty
  Improved meteorology model (parameterization, etc.) from Yixuan, Dalin, Kayo
Surface fluxes (a.k.a., prior)
  Fossil fuel (FFDAS: global 10km; waiting for high-res from Gurney)
  Bio-flux: currently from VEGAS running inside WRF;
  VEGAS: part of IPCC 2001-2013 and Global Carbon Project
Lateral boundary conditions
  Boundary CO2 concentration from the global LETKF-Carbon DA product (assimilates flask, aircraft, satellite data). This system can also provide an alternative to the FFE/Bio fluxes, albeit at lower resolution but possibly better constrained.
  Can also use other product such as CarbonTracker, subject to a delay

## Slide 3: Forward transport of CO2 with WRF-Chem
Operational forecast of CO2 set up for DC/Baltimore
FF and bio fluxes as separate tracers; CO2/CH4
48 hour forecast takes around 5 hours on 4 nodes of Deepthought 2
3 domains: 9km,3km,1km
Outer domain (9km)
Inner domain (1km)
2 days at AmeriFlux VA site
(Note daytime CO2 uptake in Feb)
6 days WRF-VEGAS simulation
Flux comparison: flux tower vs model

## Slide 4: Components of urban carbon modeling/DA system Data assimilation: The Local Ensemble Transform Kalman Filter (LETKF-Carbon)
Development
  Efficient algorithm by Hunt et al. (2007), following Kalnay, Ott, …
  LETKF initial coding by T. Miyoshi (Ph.D thesis with E. Kalnay: global version LETKF-SPEEDY, LETKF-GFS; regional version LETKF-WRF)
  Application to carbon by Kang (2009 thesis), Kang et al. (2011, 2012)
  Coupled atmo-land carbon DA system (Jia et al. 2014; Liu et al. 2017; collaboration with CAS/IAP, UC Berkeley, DOE/PNNL, S. Penny, T. Sluka): can assimilate fluxes (not as prior); real-data GV/OCO2
Advanced DA techniques
  Short assimilation window: capture fast atmo variations; accommodate continuous measurements from tower, ground, aircraft
  Possible without prior (better with good prior)
  DA-model outer-loop to allow easy model switching
  Near real-time setup: LETKF-Carbon using GEOSChem-VEGAS-FFDAS currently running to Fall 2016 with ObsPack/OCO2

## Slide 5: Sample results: Global LETKF-Carbon with GEOSChem
Black: ‘Nature’ (VEGAS model simulation)
Green: Assimilation result (ensemble mean)
Yellow: Uncertainty (ensemble spread)
Experimental setup:
- GlobalView-CO2 flask network (2001-2015)
- OCO2 satellite column XCO2 (2014-2016)
- 6hr assimilation window
- 80 ensemble members
- Additive inflation
- Prior flux (FFE+land+ocean) = 0.01
Surface carbon fluxes 2001-2016
(global total; GtC/y)
Nature Assimilated (Ens.mean)
Winter
Surface carbon fluxes
Results
Captures seasonal cycles and interannual variability; amplitude a bit smaller compared to ‘Nature’: which is closer to truth?
Agreement in major emission centers of North America, Europe, East Asia
Larger differences in India, Africa

## Slide 6: Planned work LETKF-WRF-Carbon
WRF-CO2 forward simulation
  Comparison with tower, satellite and low-cost sensor data
  Test CO2 sensitivity to model parameterization choices (PBL scheme, PBL height, etc.)
  Incorporate/use improved meteorology (parameterization choices, boundary conditions, etc.) from Yixuan
Couple WRF-CO2 into the LETKF-Carbon framework (Cory with the support of Yun Liu?)
OSSE experiments with LETKF-WRF-Carbon
Carbon data assimilation with LWC for tower, satellite and low-cost sensor data

## Slide 7
Model drivers Models Assimilation Observations
Carbon data assimilation strategy for urban GHG Monitoring
Possibilities and considerations
Uncertainty in atmospheric transport quantified naturally by meteorology ensemble
  Inter-model ensemble
  Likely, also intra-model uncertainty, e.g., different versions of WRF
Varying type of uncertainty in different observations are accounted for and differentiated, e.g., continuous observation vs. intensive campaign; high-accuracy vs. low-precision sensors
Uncertainties in flux due to meteorology, CO2 observations, and prior emissions are simultaneously quantified
LETKF can also do back-trajectory to support field campaign, via ensemble tracer release
Work ahead
Forward transport modeling with WRF
  boundary conditions: lateral CO2; emissions
  First step of DA
  useful for benchmarking airplane measurements
Emission prior
Bio prior: Carbon cycle modeling: bio flux
LETKF-WRF-Carbon DA
Slide from June 2015

## Slide 8: Low-cost sensors: plan
Network design, development and deployment
  NIST OSSE simulation by Lopez-Coto et al.: ~100 low-cost sensors
  Co-locating with EarthNetwork WeatherBug stations. Will make a software version that utilizes WIFI instead of SIM card, and a hardware package that can well integrate into WeatherBug station. Both based on our Raspberry-Pi package.
  Expanding from our existing network of ~20 stations (currently ~10 sites) on rooftop, backyard, and tower of government agencies, schools, and private citizens
  Beyond Raspberry-Pi: Model A

## Slide 9
1
2
3
4
Mini-SENSE
Low-cost sensor array
The experimental mini-network of ~20 sensor packages being deployed as a testbed. Colored dots indicate OCO2 tracks. Sample data from numbered location are shown below.
Sensor locations
7 days of data (Mar2-Mar9, 2016) from 4 sensor stations identified in the map above. Vertical offsets exist; the variabilities are meaningful.

## Slide 10: Model A: Revision 3

## Slide 11: Low-cost sensors plan II
Sensor calibration
  Co-location with WeatherBug, MDE, DOEE instruments
  2-3 sensors at one site
  Longer-term drift (> 1 month): Lab and site
  Field calibration with small tank?
  Software-based network calibration
Other sensors
  We have done some testing of low-cost sensors for CH4 (Figaro), PM(Shinyei), Alphasense CO/O3/SO2/NO2
  Working with Joe Hodges and others at NIST to establish the accuracy (Shaun Howe and undergrads?)

## Slide 12: Low-cost sensors plan III
Data processing and analysis
  algorithm and software enables low-accuracy (~30ppm) to medium-accuracy (5-10ppm)
  automation of software to deal with the large number of sensors
Data Management
  MYSQL database, web/phone display, user account, ease of download, server-side data service
  We’d like to work with NIST on developing a modern computer science-based data management standard that would be particularly suitable for the management of large network of data, while allowing both interactive display and access to large-data quantity for the modeling and data assimilation needs

## Slide 14: Carbon cycle modeling and data assimilation for NIST-UMD Baltimore-Washington Project
An update
People:
Ning Zeng, Eugenia Kalnay, Cory Martin
Collaborators: Yun Liu, Steve Penny, Travis Sluka, Ghassem Asrar, Inez Fung
Past contributions from: Ji-Sun Kang, Takemasa Miyoshi, B. Jian, Z. Chen