NCDAQ 2000 Summer Air Quality Study

NCDAQ 2000 Summer Intensive:  Summary of University of Maryland Flight Activities

Bruce Doddridge, Principal Investigator: 301-405-7628(P); 301-314-9482(F); bruce@atmos.umd.edu

4/29/2001 Revision

Instrument Suite

The University of Maryland research-grade instrument suite is summarized in the following table, with individual instruments detailed more specifically below.

# Table. University of Maryland Aztec-D Proposed Instrument Suite

Parameter		Temporal	Detection		Technique (Instrument)

Resolution	Limit

Receiver mounted on upper fuselage

Lat./Long.		10 s		15 m			GPS (Garmin GPS-90)

Mounted on upper fuselage

Static pressure		10 s		5 mb			transducer (Rosemount 1008)

Probe mounted between sampling inlets

Temperature		10 s		0.5C			thermistor (Rustrak RR2-252)

Relative humidity	10 s		2 %			thin capacitive film (Rustrak RR2-252)

Samples from rear-facing inlet

O3			4 s		  1 ppbv			UV photometric (TEI 49C)

CO			1 min*		20 ppbv			modified NDIR/GFC (TEI 48)

SO2			1 min*		30 pptv			modified pulsed-fluorescence (TEI 43C)

Samples from front-facing isokinetic inlet

Aerosol absorption	1 min**		0.9(106 m-1		modified photometric (Rad. Res. PSAP)

* From 10 s data

** From 1 s data

Position was measured and stored using Global Positioning System, GPS (Garmin GPS-90).  Latitude and longitude were recorded at 10 s temporal resolution within the GPS unit, downloaded post-flight to a laptop personal computer (PC) and subsequently integrated with the other flight data using commercial software.

Temperature and relative humidity were measured using a thermistor and capacitive thin film, respectively, with a regularly calibrated Rustrak RR2-252 RH probe (EIL Instruments Inc., Hunt Valley, MD).  The instrument is capable of 0.5C precision in temperature and 2% precision in humidity with a 30 s response.  Pressure was measured using a Rosemount Model 2008 pressure transducer, capable of 5 mb precision, and calibrated regularly to a laboratory standard.

Ozone data were acquired by a commercial optical instrument using absorption of UV radiation at 254 nm (Thermo Environmental, TEI Model 49, Franklin, MA), modified for increased (4 s) temporal response.  This instrument was routinely compared to an in-house primary O3 calibrator (TEI Model 49PS) being fed on zero grade air (Scott-Marrin).

For observations of CO, a high-performance modified (Dickerson and Delany, 1988) commercial (TEI Model 48) nondispersive infrared (NDIR) gas filter correlation analyzer was used.   This instrument has a detection limit of ~24 ppbv (S:N=1:1 for ±2σ noise) for a 1-min mean of 10 s data, and was calibrated using CO working standards (1-2 ppmv CO in nitrogen; Scott-Marrin, Riverside, California) in turn referenced to a National Institute of Standards and Technology(NIST)/Standard Reference Material (1677c 9970 ppbv CO in nitrogen, certified; NIST, Gaithersburg, Maryland). This instrument is capable of ~1% precision determined for a 1-min mean of 10 s data. The CO instrument has undergone formal international calibrations (Novelli et al., 1998) under a WMO protocol (Doddridge, 1995).

A modified commercial pulsed-fluorescence detector was used for measurements of ambient SO2.  Modifications, the most significant of which is to add a zeroing filter a chemical (carbonate) scrubber for SO2 to the commercial instrument, and the subsequent field and laboratory evaluations of the modified system prototype are reported by Luke (1997).  The instrument is capable of a detection limit of 30 pptv for averaging interval on the order of 25 min, expected to be significantly higher at 1 min integration times typical of research flight data, but still useful for emissions work.

Data acquisition for the continuous meteorological and trace gas instruments at 10-sec time resolution was effected using a Rustrak Ranger II (EIL Instruments Inc., Hunt Valley, MD) data logger.  Raw data are viewed by the mission scientist in flight as a real time status check of instrument performance and ambient air characteristics.  Data were downloaded after each flight to a laptop PC for initial field processing under Windows NT then processed further on a DEC AlphaStation networked UNIX workstation using established routines.

Light absorption due to aerosol was be measured using a Particle/Soot Absorption Photometer (PSAP, Radiance Research, Seattle, WA), by transmission of 565 nm light through a filter in turn through which sample air is drawn.  Corrections for signal non-linearity and aerosol scattering were made according to Bond et al. (1999).  The detection limit for S:N=2 is 0.9(106 m-1. Aerosol absorption data were logged as 1-minute averages of 1-second data during research flights using custom acquisition software.

Bond, T.C., T.L. Anderson, and D. Campbell, Calibration and Intercomparison of Filter-based Measurements of Visible Light absorption by aerosols, Aerosol Sci. Technol., 30, 582-600, 1999.

Dickerson, R. R., and A. C. Delany, Modification of a Commercial Gas Filter Correlation CO Detector for Enhanced Sensitivity, J. Atmos. Oceanic Tech., 5, 424-431, 1988.

Doddridge, B.G., Report of the Working Session on Measurement Techniques and Standards, in Report of The WMO Meeting of Experts on Global Carbon Monoxide Measurements, P. C. Novelli and R. M. Rosson (eds), WMO TD-NO. 645, pp. 8-11, 1995.

Luke, W.T., Evaluation of a Commercial Pulsed Fluoroescence Detector for the Measurement of Low-Level SO2 Concentrations During the Gas-Phase Intercomparison Experiment, J. Geophys. Res., 102, 16,255-16,265, 1997.

Novelli, P.C., V.S. Connors, H.G. Reichle, Jr., B.E. Anderson, C.A. Brenninkmeijer, E.G. Brunke, B.G. Doddridge, V.W.J.H. Kirchoff, J.K.S. Lam, K.A. Masarie, T. Matsou, D.D. Parrish, H.E. Scheel, L.P. Steele, An Internally Consistent set of Globally Distributed Atmospheric Carbon Monoxide Mixing Ratios Developed Using Results From an Intercomparison of Measurements, J. Geophys. Res., 103, 19285-19293, 1998.

Original Flight Plans

Several flight plans were selected at project inception, assuming operations commencing from the FBO at Raleigh-Durham International Airport (RDU) 35º52.654'N, 78º47.245'W, Elev. 435 ft.  An abridged subset of these original draft plans are listed below, as they provide a useful reference for the flight summary immediately following.

Plan A:  Point Source/Triad

This plan supports objectives 2.–7. by characterizing transport from point sources along the NC-VA border, while investigating air quality along Charlotte-Greensboro and Triad-Triangle (Raleigh, Durham, and Chapel Hill) transport corridors, and evaluating continuous tower and radar profiler measurements in the vicinity of Raleigh.  Ideal meteorological conditions would be a ridge-induced stagnation event with clear sky and light westerly to southwesterly winds.  The aircraft will depart RDU and perform vertical profile spirals from the surface (low approach to ~10 m AGL over the active runway; see runway elevations listed below) up to 2.7 km MSL at 100 m min-1 climb rate over the following airports:

5W5		Triple W				35º37.225'N, 78º42.013'W, Elev.   240 ft MSL

EXX		Davidson County			35º46.866'N, 80º18.181'W, Elev.   720 ft MSL

MWK	Mount Airy Surry County		36º27.580'N, 80º33.178'W, Elev. 1250 ft MSL

W63		Marks Municipal			36º35.748'N, 78º33.609'W, Elev.   420 ft MSL

Traverses between spiral locations will be performed at minimum allowable altitude (3,500 ft MSL to the west and 1,500 ft MSL to the east), this in order to further characterize the PBL.  The spiral location ordering in this pattern, similar to those below, is designed to maximize the possibility of a Lagrangian observational result.  That is, under prevailing wind conditions (assuming that weak southwesterly to westerly flow will characterize most regional pollution episodes studied here) the same air parcel might perhaps be sampled in the vertical twice at different geographical locations, facilitating mesoscale transport model evaluation and cross-corridor mass balance calculations.  Operating in the afternoon will characterize the most active photochemical ozone and particulate haze production.  Morning flights can be conducted as a contrast to PM operations, to investigate AM development of the PBL, mixing down of remnant stratified pollution layers aloft, and in situ photochemical smog production over the region.

Plan B:  Raleigh Area

This plan supports objectives 3.–7. by characterizing air quality upwind and downwind of the city of Raleigh, and evaluating continuous tower and radar profiler measurements in that vicinity.  Ideal meteorological conditions would be a ridge-induced stagnation event with clear sky and light westerly winds, although winds from the southwest would suffice.  The aircraft will depart RDU and perform vertical profile spirals from the surface (low approach to ~10 m AGL over the active runway; see runway elevations listed below) up to 2.7 km MSL at 100 m min-1 climb rate over the following airports:

5W5		Triple W				35º37.225'N, 78º42.013'W, Elev.   240 ft MSL

JNX		Johnston County			35º32.457'N, 78º23.422'W, Elev.   170 ft MSL

5W8		Siler City Municipal			35º42.179'N, 79º30.319'W, Elev.   610 ft MSL

HNZ		Henderson-Oxford			36º21.689'N, 78º31.755'W, Elev.   530 ft MSL

RWI		Rocky Mount-Wilson Regional	35º51.295'N, 77º53.574'W, Elev.   160 ft MSL

Again, traverses between spiral locations will be performed at minimum allowable altitude (1,500 ft MSL to the north and 2,500 ft MSL to the south).  A mid-plan brief (usually less than 20 minutes) refueling layover may be required, this depending somewhat on the strength of westerly winds encountered aloft on the westerly traverse 5W5–EXX.  As above, afternoon operation will characterize the most active photochemical ozone and particulate haze production, but morning flights can be conducted to investigate AM development of the PBL, mixing down of remnant stratified pollution layers aloft, and anthropogenic (industrial/transport/other) pollutant input across the city of Raleigh.

Research Flight Summary

Times are UTC.  Spiral heights are in K feet MSL and approximate.

00/08/08 RF-01	00808-01.xls		Plan: FerryW29-RDU

# Flight time:  1243-1456 (133 min)

Spirals:		u/d		Time				Height

5W501		dn		1424-1448			6.5

00/08/08 RF-02	00808-02.xls		Plan: WWW Survey Profile

# Flight time:  1826-1916 (  50 min)

Spirals:		u/d		Time				Height

5W502		up		1840–1901			6.5

00/08/08 RF-03	00808-03.xls		Plan: A. Point Source/Triad

# Flight time:  1938-2253 (195 min)

Spirals:		u/d		Time				Height

EXX01		up		2020–2053			9.5

W6301		up		2142–2159			6.5

5W503		dn		2230–2244			6.5

00/08/09 RF-04	00809-04.xls		Plan: A. Point Source/Triad

# Flight time:  1237-1604 (207 min)

Spirals:		u/d		Time				Height

5W504		up		1252–1316			6.5

EXX02		dn		1351–1432			9.5

W6302		up		1522–1540			6.5

00/08/09 RF-05	00809-05.xls		Plan: B (variant.) Cross-Raleigh Corridor Transport

# Flight time:  1822-2100 (158 min)

Spirals:		u/d		Time				Height

DAN01		up		1848-1907			6.5

TDF01		dn		1914-1934			6.5

5W505		up		1958-2015			6.5

JNX01			dn		2022-2044			6.5

00/08/10 RF-06	00810-06.xls		Plan: Ferry RDU-W29

# Flight time:  1159-1342 (103 min)

Spirals:		u/d		Time				Height

None

NC Research Hours	14:06

Spirals:

AIRXX	AIR = airport identifier (see below)

XX  = profile identifier (chronological/numeric)

Airports:

5W5		Triple W				35º37.225'N, 78º42.013'W, Elev.   244 ft MSL

DAN		Danville Regional			36º34.286'N, 79º20.194'W, Elev.   572 ft MSL

EXX		Davidson County			35º46.866'N, 80º18.181'W, Elev.   733 ft MSL

JNX		Johnston County			35º32.457'N, 78º23.422'W, Elev.   165 ft MSL

TDF		Person County				36º17.095'N, 78º59.049'W, Elev.   609 ft MSL

W29		Bay Bridge				38º58.574'N, 76º19.785'W, Elev.     15 ft MSL

W63		Marks Municipal			36º35.748'N, 78º33.609'W, Elev.   421 ft MSL

SUMMARY OF KEY SCIENCE RESULTS

1. Summer 2000 Synoptic Summary

For a summary of the 2000 summer ozone season, including hypertext links to weather products and other potentially useful resources see

http://www.meto.umd.edu/~ryan/summary00.html

2. Aircraft-WRAL Tower Comparison:

Profile		Profile Time		Comments on Agreement

(EST)

5W501	0924-0948		Excellent

5W502	1340–1401		Poor (tower ~ aircraft + 25 ppbv)

5W503	1730–1744		Poor near surface (T ~ AC  8 ppbv) and aloft (T ~ AC + 15 ppbv)

5W504	0752–0816		Fair (within 5-10 pbbv)

5W505	1458-1515		Poor (T~ AC + 20-25 ppbv)

It appears 5W5 profiles are not always comparable to WRAL Tower.  This seems worse during the afternoon.  The WRAL tower is situated 15 km from 5W5, and borders a major interstate highway (US-70) The possibility exists that auto emissions contribute to local O3 characteristics.